Features	P01

Package Drawing & Pin out	P01

Technical Characteristics 	P02

Matching Network 	P02

Nominal Response	P03

Maximum Ratings	P04

Marking & Packaging	P04

Features

- RF SAW Filter

- 942.5 MHz Center Frequency

- Ceramic package for Surface Mounted Technology

- RoHS Compliant, Lead-free soldering

Package Drawing & Pin out

The product is in conformance with the European RoHs Regulation 2002/95.

Te

Technical Characteristics

| Electrical Parameters | Unit | Minimum | Typical (1) | Maximum |
| --- | --- | --- | --- | --- |
| Center Frequency fo | MHz |  | 942.5 |  |
| Insertion Loss within 925 ~ 960 MHz | dB | - | 2.8 | 4.0 |
| Amplitude ripple within 925 ~ 960 MHz | dB | - | 1.1 | 2.3 |
| Attenuation |
| From 0 to 800 MHz | dB | 50 | 63 | - |
| From 800 to 880 MHz | dB | 40 | 48 | - |
| From 880 to 905 MHz | dB | 35 | 43 | - |
| From 980 to 982 MHz | dB | 20 | 27 | - |
| From 982 to 1005 MHz | dB | 23 | 28 | - |
| From 1005 to 1025 MHz | dB | 29 | 33 | - |
| From 1025 to 1760 MHz | dB | 40 | 50 | - |
| From 1760 to 2300 MHz | dB | 30 | 41 | - |
| From 2300 to 3000 MHz | dB | 20 | 28 | - |
| Source Impedance (Single ended) | Ohms |  | 50 (2) |  |
| Load Impedance (Single ended) | Ohms |  | 50 (2) |  |
| Package type & size |
| Length x Width | mm |  | 3.0 x 3.0 |  |
| Height | mm |  |  | 1.50 |
| Pin Out |
| Input | 2 | Output | 5 |
| Case Ground | 1,3,4,6 | To be grounded | 1,3,4,6 |

Notes :

- Typical values are nominal performances at room temperature

- Not external matching circuit is required

Measurement Circuit

Nominal Frequency Response (Measurements)

Maximum Ratings

| Storage Temperature Range | °C | [-40°C ; +85°C] |
| --- | --- | --- |
| Operating temperature | °C | [-30°C ; +85°C] |
| DC voltage | V | 3 max |
| RF Power Dissipation | dBm | 15 max |

Marking

Line 1: "NNNN" is the reference to Temex Part number with only the last 4 digits

Line 2: EYWWZZ is the date code as:

E: Partner identifier.

Y: last digit of the year.

WW: number of week in the year

ZZ: Lot number in the week (from AA to ZZ).

Packaging

1 – Temex Label

2 – ESD Prevention Label

3 – Pb Free Label

# Text boxes

TMX W329

SAW Front-End Filter – GSM  Rx - RF

Specification (Rev 2)

1, 3, 4, 6

PCB Footprint

W329

E033AA

| Pin Configuration |
| --- |
| Input | 2 |
| Output | 6 |
| Case Ground | 1, 3, 4, 5, 7, 8 |

1Kpcs/reel